## Slide 1: Using Fixed-Point Approximations to Accelerate Integer Division
Lucas Dutton (McMaster University)
with Christopher Anand (McMaster University)
with IBM Collaborators:
Robert Enenkel (IBM Toronto)
Silvia Melitta Müller (IBM Böblingen)
Curtis D’Alves (IBM Toronto)
SONAD 2026
May 1, 2026
Notes: Add Curtis

## Slide 2: Elementary Functions
Scientific Computation
Tradeoff between
Precision + Accuracy
Efficiency
Example: sin/cos
ML & AI Applications
Less Precision + Accuracy
More Efficient
Example: Activation functions (sigmoid)
Database & Cryptographic Kernels
Exact Computations
Fixed Precision
Constant-time execution: Cannot use floating-point
Notes: Constant-time: Cannot use FP + Have to read the entire table into memory (no single-element access)

## Slide 3: SRT (HW)
+ Fast Recurrence
+ Bit-level redundant representation
+ Space-Efficient
– Linear Convergence
Newton
Raphson
(HW/SW)
+ Quadratic Convergence
- Done with Floating-Point?
Division Techniques

## Slide 4: What I’ll Show (32-Bit Int Div)
(1) Multi-Table Lookup + Normalization
- Converting Integers to Fixed-Point Numbers
- ~14 bits of accuracy
(2) Assembling the Reciprocal
- NR iteration
- 14 bits of accuracy -> ~28 bits
(3) Calculating Quotient
Trial Quotient + Remainder
“Last-bit” Correction
(4) Implementation + Extensions
RISC-V
Other Integer Precisions

## Slide 5: Lookup Tables
Quick way of obtaining initial approximation of a function
Use most-significant fraction bits of input as index into table

## Slide 6: Start with a “standard” table
The T-table: regularly-spaced fixed-point values of the function interval
Notes: x-axis: Individual input values in an interval. There are 2^15 = 32768 values in total
y-axis: The ulp error of each value

## Slide 7: Start with a “standard” table
The T-table: regularly-spaced fixed-point values of the function interval
Notes: x-axis: Individual input values in an interval. There are 2^15 = 32768 values in total
y-axis: The ulp error of each value

## Slide 8: Add a linear correction
S-table: Linear correction values relative to the T-table
Notes: x-axis: Individual input values in an interval. There are 2^15 = 32768 values in total
y-axis: The ulp error of each value

## Slide 9: Add a linear correction
S-table: Linear correction values relative to the T-table
Notes: x-axis: Individual input values in an interval. There are 2^15 = 32768 values in total
y-axis: The ulp error of each value

## Slide 10: Normalization: Integers -> Fixed-Point as input to recip
Want to fit denominator
to
Method: Shift out all leading zeros to the left
Example:
  Integer becomes
  Integer also becomes
  Integer becomes
Precision: 32 bits
Fraction: 31 bits

## Slide 11: Recip Computation

## Slide 12: Recip Computation
(1) Table Lookups

## Slide 13: Recip Computation
(2) Calculate + Subtract Linear Correction
Notes: - Element-width selection: Allows for mixed-precision performance

## Slide 14: Recip Computation
(3) Fixed-Point NR Iteration

## Slide 15: Now for the Quotient

## Slide 16: Now for the Quotient
  We have:
  the normalized denominator
  the computed recip approx

## Slide 17: Now for the Quotient
  From and numerator , compute:
    Trial quotient
    Trial remainder

## Slide 18: Now for the Quotient
  is our error
  Compute a correction
  Add correction to
  What are the bounds on ?

## Slide 19: Outline: Proof of Correctness
Initial 16-bit table approximation: Bounds obtainable through exhaustive testing
32-bit Reciprocal approximation: Also can be exhaustively tested
Full div bounds: Cannot be exhaustively tested
  Except for an important subset: Large numerator and small denominator
  Other cases: Prove analytically!
  Gives us the correction factor from previous slide

## Slide 20: RISC-V ISA + Vector Extension
32 vector registers, VLEN-bit wide
Global parameters:
  vl: #elements per vector op
  SEW (Selected Element Width): size of input/output elements
  LMUL: Group Multiplier; size of vector group
VLMAX = LMUL * VLEN / SEW (limit of vl)
Implementation parameter
Example:
VLEN=128, LMUL=2, vl=7, SEW=32b: A vadd.vv op performs 32-bit integer add on 7 element vectors

## Slide 21: RISC-V Implementation (Constant time for Crypto)
Procedure | # SIMD Instructions
Recip: Approx | 25
Div: Correction procedure | 18
Implemented in C using RVV intrinsics
  Operations done with max group size (EMUL m8) for highest throughput.
  Only integer operations used.
Extensions
  8-bit, 16-bit: Lookup + 1-bit correction. Fast!
  64-bit: Use 32-bit recip + 3 extra trial quotient+remainder iterations.
8-way unrolled, working with 8 instruction groups + wide register groups
Notes: SIMD (Internal) Ops
Look into ARM/POWER (not constant time div)
Select a certain subset of RISCV instructions to ensure constant time
Implementor can freely change parameters and the software will adapt; But only works for matrix ops/dot product etc.
Doesn’t quite work with operations like table lookups
The bulk of numerical computations is becoming more hardware independent, but performance-critical elementary functions are going the opposite way – need to optimize for architecture (in our experience)

## Slide 22: FP32 Single-Instruction Recip Estimate
VRCPSS
Accurate to
12 bits
#Instructions for DP:
10
vfrec7
Accurate to
7 bits
#Instructions for DP:
13
xvresp
Accurate to
14 bits
#Instructions for DP:
10
Proposed HW
POWER
RISC-V
Accurate to
20 bits
#Instructions for DP:
7
x86
Using same algorithmic approach as this talk for FP32 recip
See “A Multi-Table Approach to Floating-Point Function Approximation”
Notes: No direct comparison, but this is the closest comparison relative to other FP recip estimates

## Slide 23: Conclusions + Future Work
Have an efficient, constant-time integer divide
Implemented in RISC-V
Future work:
  Hardware implementations for further acceleration
Related paper:
  Inexactness and Correction of Floating-Point Reciprocal, Division and Square Root

## Slide 24
Thanks!
Questions?

## Slide 25: Detailed T-Table & S-Table
Notes: x-axis: Individual input values in an interval. There are 2^15 = 32768 values in total
y-axis: The ulp error of each value